## Slide 1: Noida Institute of Engineering and Technology, Greater Noida
Introduction
Mr. Lakshman Singh
Unit: 1
COMPUTER SYSTEM ORGANIZATION (AMCA 0104)
MCA-I SEM

## Slide 2
Syllabus

## Slide 3
Syllabus

## Slide 4
Introduction
Digital computers and Number system
Logic gates
Boolean Algebra
Map simplification
Combinational circuits
Sequential circuits
Look ahead carry adders
Data types and complements
Contents

## Slide 5
Fixed point representation
Fixed point addition and Subtraction
Floating Point representation
Booth’s multiplication algorithm
IEEE 754 floating point standards
Contents Cont..

## Slide 6
Discuss the basic concepts and structure of computers.
Understand concepts of register transfer logic and arithmetic operations.
Explain different types of addressing modes and memory organization.
To discuss different types of number systems and their significance and usage
Course Objective

## Slide 7
Before learning the concepts of Basic Electronics and Computer Organization, you should have a basic knowledge of functional units of a computer system.
The basic knowledge of mathematics.
The knowledge of English language upto a satisfactory level.
Prerequisite

## Slide 8
Digital computer and Number systems
Topic

## Slide 9
To discuss about digital computer, different number systems, bases and the conversion of one number system to another.
Representation of number systems in unsigned forms.
Topic objective

## Slide 10
Digital Computer (Definition):
An electronic computer in which the input is discrete rather than continuous, consisting of combinations of numbers, letters, and other characters written in an appropriate programming language and represented internally in binary notation.
Capable of solving problems by processing information in discrete form.
The first electronic digital computer was developed in the late 1940s and was used primarily for numerical computations. By convention, the digital computers use the binary number system, which has two digits: 0 and 1. A binary digit is called a bit.
Introduction (CO1)

## Slide 11
A computer system is subdivided into two functional entities: Hardware and Software.
The hardware consists of all the electronic components and electromechanical devices that comprise the physical entity of the device.
The software of the computer consists of the instructions and data that the computer manipulates to perform various data-processing tasks.

## Slide 13
The Central Processing Unit (CPU) contains an arithmetic and logic unit for manipulating data, a number of registers for storing data, and a control circuit for fetching and executing instructions.
The memory unit of a digital computer contains storage for instructions and data.
The Random Access Memory (RAM) for real-time processing of the data.
The Input-Output devices for generating inputs from the user and displaying the final results to the user.
The Input-Output devices connected to the computer include the keyboard, mouse, terminals, magnetic disk drives, and other communication devices.

## Slide 14
Number System (Definition):
A number system of base, or radix, r is a system that uses distinct symbols for r digits.
Numbers are represented by a string of digit symbols.
For example- The decimal number system in everyday use employs the radix 10 system. The 10 symbols are 0,1,2,3,4,5,6,7,8, and 9.
The string of digits 724.5 is interpreted to represent the quantity
7 X 102 + 2 X 101 + 4 X 100 + 5 X 10-1
Introduction (CO1)

## Slide 15
Unsigned numbers don’t have any sign, these can contain only magnitude of the number.
So, representation of unsigned binary numbers are all positive numbers only.
For example, representation of positive decimal numbers are positive by default. We always assume that there is a positive sign symbol in front of every number.
Unsigned Numbers (CO1)

## Slide 16
Example-1: Represent decimal number 92 in unsigned binary number.
Simply convert it into Binary number, it contains only magnitude of the given number. = (92)10 = (1x26+0x25+1x24+1x23+1x22+0x21+0x20)10 = (1011100)2
It’s 7 bit binary magnitude of the decimal number 92.
Unsigned Numbers (CO1)

## Slide 17
Converting between bases (CO1)
Other Base System to Decimal System
Steps
Step 1 − Determine the column (positional) value of each digit (this depends on the position of the digit and the base of the number system).
Step 2 − Multiply the obtained column values (in Step 1) by the digits in the corresponding columns.
Step 3 − Sum the products calculated in Step 2. The total is the equivalent value in decimal.

## Slide 18
Converting between bases (CO1)
Example
Binary Number :111012
Calculating Decimal Equivalent :
Step Binary Number Decimal Number: 1
111012=((1 × 24) + (1 × 23) + (1 × 22) + (0 × 21) + (1 × 20))10
Step 2
111012 =(16 + 8 + 4 + 0 + 1)10
Step 3
111012=2910
Binary Number 111012 = Decimal Number 2910

## Slide 19
Converting between bases Cont.. (CO1)
Step | Octal Number | Decimal Number
Step 1 | 258 | ((2 × 81) + (5 × 80))10
Step 2 | 258 | (16 + 5 )10
Step 3 | 258 | 2110
Other Base System to Non-Decimal System
Step 1 − Convert the original number to a decimal number (base 10).
Step 2 − Convert the decimal number so obtained to the new base number.
Example: Octal Number : 258
Calculating Binary Equivalent
Step 1 Convert to Decimal
Octal Number 258 = Decimal Number 2110

## Slide 20
Write counting upto 100 in Octal and Hexadecimal?
Write counting upto 20 in base = 3 and base =5?
Convert the following numbers with the indicated bases to decimal: (12121)3; (4310)5; (50)7; and (198)12.
Convert the following decimal numbers to binary: 1231; 673; and 1998.
Daily Quiz

## Slide 21
In the last lecture we have discussed about
Number systems, base of number systems and the conversion of one number system to another.
Representation of number systems in unsigned forms.
Recap

## Slide 22
Signed integer representation
Fixed and floating point representation
Topic

## Slide 23
To discuss about representation of negative numbers In signed magnitude, 1’s complement and 2’s complement representation schemes.
How to represent the numbers in fixed and floating point forms.
What are different character codes used to represent characters.
Topic objective

## Slide 24
To represent negative integers, we need a notation for negative values.
It is customary to represent the sign with a bit placed in the leftmost position of the number since binary digits.
The convention is to make the sign bit 0 for positive and 1 for negative.
Example: there are 3 different ways to represent -9 with eight bits
Signed Integer Representation (CO1)

## Slide 25
The floating-point representation of a number has two parts.
The first part represents a signed, fixed-point number called the mantissa.
The second part designates the position of the decimal (or binary) point and is called the exponent.
The fixed-point mantissa may be a fraction or an integer. For example, the decimal number + 6132.789 is represented in floating-point with a fraction and an exponent as follows:
  Fraction Exponent
+ 0 .6132789 + 04
Fixed and Floating Point Representations (CO1)

## Slide 26
1. Gray Code:-The advantage of the Gray code over straight binary numbers is that the Gray code changes by only one bit as it sequences from one number to the next. (Refer Table- 3.5)
2. Other Decimal Codes:-
- BCD, EBCDIC
- Excess-3, Excess-127
- 8421, 2421
- Error Detection codes (Parity bit)
Character Codes (CO1)

## Slide 27
Daily Quiz
Represent decimal number 8620 in
(a) BCD;
(b) excess-3 code;
(c) 2421 code;
(d) as a binary number
2. What is the radix of the numbers if the solution to the quadratic equation x2 – 10x + 31 = 0 is x = 5 and x = 8

## Slide 28
In the last lecture we have discussed about
How to represent negative numbers In signed magnitude, 1’s complement and 2’s complement representation schemes.
How to represent the numbers in fixed and floating point forms.
What are different character codes used to represent characters.
Recap

## Slide 29
Logic gates
Topic

## Slide 30
To discuss about the function of logic gates using different representation schemes.
Topic objective

## Slide 31
Logic Gates
The gates are blocks of hardware that produce a binary output.
There are three elementary logic gates and a range of other simple gates.
Each gate has its own logic symbol which allows complex functions to be represented by a logic diagram.
The function of each gate can be represented by a truth table or using Boolean notation.
Digital Logic (CO1)

## Slide 32
Digital Logic (CO1)

## Slide 33
Logic Gates (CO1)
The AND gate

## Slide 34
Logic Gates Continued (CO1)
The OR gate

## Slide 35
Logic Gates Continued (CO1)
The NAND gate

## Slide 36
Logic Gates Continued (CO1)
The NOR gate

## Slide 37
Logic Gates Continued (CO1)
The Exclusive OR (XOR) gate

## Slide 38
Logic Gates Continued (CO1)
The Exclusive NOR (X-NOR) gate

## Slide 39
Logic Gates Continued (CO1)
The NOT gate (or inverter)
A logic buffer gate

## Slide 40
1. Which of these are called universal gate, And why ?
2. Differentiate between ex-or and ex-nor gate.
Daily Quiz

## Slide 41
1. Simplify the Boolean function F together with the don't-care conditions d in
sum-of-products form.
F(w, x, y, z) = ∑(0, 1, 2 , 3, 7, 8, 10)
d(w, x, y, z) = ∑(5 , 6, 11, 15)
2. Which of the gates are called universal gate, And why ?
Weekly Assignment

## Slide 42
In the last lecture we have discussed about
Function of logic gates and their representation
Recap

## Slide 43
Boolean Algebra
Topic

## Slide 44
In this lecture we will discuss about-
Boolean algebra, boolean identities and show how we can minimize a boolean expression by using the identities of boolean algebra.
Topic objective

## Slide 45
Boolean algebra (CO1)
Boolean algebra is an algebra that deals with binary variables and logic operations.
The variables are designated by letters such as A, B, x, and y.
The three basic logic operations are AND, OR, and complement.
A Boolean function can be expressed algebraically with binary variables, the logic operation symbols, parentheses, and equal sign. For a given value of the variables, the Boolean function can be either 1 or 0.

## Slide 46
Boolean algebra continued.. (CO1)
Basic identities of Boolean algebra
(1) x+0=x (2) x.0=0
(3) X+1=1 (4) x.1=x
(5) X+X=X (6) X.X=X
(7) X+X’=1 (8) X.X’=0
(9) X+Y =Y+X (10) X.Y=Y.X
(11) X+(Y+Z) = (X+Y) +Z (12) X(YZ) = (XY)Z
(13) X(Y+Z) =XY+XZ (14) X+YZ= (X+Y)(X+Z)
(15) (X+Y)’ = X’Y’ (16) (XY)’=X’+Y’
(17) X’’=X

## Slide 47
Boolean algebra continued.. (CO1)
Example: The expression can be simplified using Boolean algebra.
F = ABC+A BC'+ A 'C = AB(C +C ')+ A 'C = AB +A 'C
Note that(C +C)' = 1 by identity 7 and AB ·1 = AB by identity 4.
we can make logic diagram for both (original and minimized) expressions and show how the hardware requirement is minimized by minimizing the boolean expressions using boolean identities.

## Slide 48
1. Simplify the following expressions using Boolean algebra.
A + AB b. AB + AB‘ c. A' BC + AC d. A'B +ABC' + ABC
2. Given the Boolean function
F = xy’z + x’y’z + xyz
a. List the truth table of the function.
b. Draw the logic diagram using the original Boolean expression.
c. Simplify the algebraic expression using Boolean algebra.
Daily Quiz

## Slide 49
In the last lecture we have discussed about
Boolean algebra, boolean identities and show how we can minimize a boolean expression by using the identities of boolean algebra.
Recap

## Slide 50
Combinational and sequential circuits.
Minimization of boolean expressions using K-map method.
Topic

## Slide 51
In this lecture we will discuss about
Combinational and sequential circuits.
Minimization of boolean expressions using K-map method.
Topic objective

## Slide 52
Combinational and sequential circuits (CO1)
Combinational Circuits
A combinational circuit is a connected arrangement of logic gates with a set of inputs and outputs.
At any given time, the binary values of the outputs are a function of the binary combination of the inputs.
n input variables
m output variables
Figure 1.1 Block diagram of a combinational circuit

## Slide 53
Combinational and sequential circuits
continued.. (CO1)
Sequential Circuits
A sequential circuit is an interconnection of flip-flops and gates.
The gates by themselves constitute a combinational circuit, but when included with the flip-flops, the overall circuit is classified as a sequential circuit.
Figure 1.2 Block diagram of a clocked synchronous sequential circuit

## Slide 54
Gate Minimization (CO1)
Map Simplification
The expression may be simplified using the basic relations of Boolean algebra.
However, this procedure is sometimes difficult because it lacks specific rules for predicting each succeeding step in the manipulative process.
The map method provides a simple, straightforward procedure for simplifying Boolean expressions.
The map method is also known as the Karnaugh map or K-map

## Slide 55
Gate Minimization Cont.. (CO1)
This method may be regarded as a pictorial arrangement of the truth table which allows an easy interpretation for choosing the minimum number of terms needed to express the function algebraically.
Each combination of the variables in a truth table is called a minterm. 2 variables and 3 variables maps are shown below-

## Slide 56
Gate Minimization Cont.. (CO1)
Example: simplifies the following Boolean function using K-map method
F(A, B, C) = ∑ (3, 4, 6, 7)
The simplified function is
F = AC' + BC
Consider another example with don’t care minterms-
F(A,B,C) = ∑(0,2,6) d(A,B,C) = ∑(1,3,5)
The map with don’t care conditions is
The simplified function is
F= A’ + BC’
 | B’C’ | B’C | BC | BC’
A’ |  |  | 1 | 
A | 1 |  | 1 | 1
 | B’C’ | B’C | BC | BC’
A’ | 1 | X | X | 1
A |  | X |  | 1

## Slide 57
1. Simplify the following Boolean functions using three and four-variable maps.
F(A,B,C) = ∑(0, 1,5, 7)
F(A,B,C) = ∑(1,2,3,6,7)
F(A,B,C,D) = ∑(0, 2,4,5,6, 7,11,15)
F(A,B,C,D) = ∑(0, 2,4,5,6, 7, 8, 10, 13, 15)
2. Simplify the Boolean function F together with the don't-care conditions d in
sum-of-products form.
F(w, x, y, z) = ∑(0, 1, 2 , 3, 7, 8, 10)
d(w, x, y, z) = ∑(5 , 6, 11, 15)
Daily Quiz

## Slide 58
In the last lecture we have discussed about
Combinational and sequential circuits.
Minimization of boolean expressions using K-map method.
Recap

## Slide 59
Digital components
Topic

## Slide 60
To discuss about
Various digital components used in the building of digital equipments
Topic objective

## Slide 61
Digital Components (CO1)
Integrated Circuits:
Digital circuits are constructed with integrated circuits.
Integrated circuit (abbreviated IC) is a small silicon semiconductor crystal. called a chip, containing the electronic components for the digital gates.
The various gates are interconnected inside the chip to form the required circuit.
The chip is mounted In a ceramic or plastic container, and connections are welded by thin gold wires.
Examples of Digital Components
- Half Adder/Full Adder
Multiplexer/ Demultiplexer
Decoder/Encoder
Registers/Counters

## Slide 62
Decoder/Encoder (CO1)

## Slide 63
Decoder/Encoder (CO1)
A decoder is a combinational circuit that converts binary information from the n coded inputs to a maximum of 2n unique outputs. If the n-bit coded information has unused bit combinations, the decoder may have less than 2n outputs.
An encoder is a digital circuit that performs the inverse operation of a decoder.
An encoder has 2n(or less) input lines and n output lines.

## Slide 64
Multiplexer (CO1)
A multiplexer is a combinational circuit that receives binary information from one of 2n input data lines and directs it to a single output line.
The selection of a particular input data line for the output is determined by a set of selection inputs.
A 2n-to-1 multiplexer has 2n input data lines and n input selection lines whose bit combinations determine which input data are selected for the output.
SELECT |  | OUTPUT
S1 | S0 | Y
0 | 0 | I0
0 | 1 | I1
1 | 0 | I2
1 | 1 | I3
Fig-1.4 4 to 1 line multiplexer.
Table-1.1 Function Table for 4 to 1 Line Multiplexer

## Slide 65
1. Construct a 5-to-32 line decoder with four 3-to-8 line decoders with enable and one 2-to 1 line decoder. Use block diagrams similar to Fig. 2·3 (M.Mano).
2. Construct a 16-to 1 line multiplexer with two 8 to 1 line multiplexers and one 2 to 1 line multiplexer. Use block diagrams for the three multiplexers.
Daily Quiz

## Slide 66
Topic
Booth’s multiplication algorithm
IEEE 754 floating point standard.

## Slide 67
Topic objective
To discuss about arithmetic algorithms for addition and subtraction, Booth multiplication algorithm and representation of floating point numbers into IEEE 754 floating point standard.

## Slide 68
Arithmetic Algorithms (CO1)
In ordinary arithmetic, a negative number is indicated by a minus sign and a positive number by a plus sign.
Because of hardware limitations, computers must represent everything with 1's and 0's, including the sign of a number.
The convention is to make the sign bit equal to 0 for positive and to 1 for negative in the leftmost position of the number.

## Slide 69
Addition, Subtraction (CO1)
Addition and Subtraction of two signed binary numbers when negative numbers are in 2' s complement form is very simple and can be stated as follows
Take the 2's complement of the subtrahend (including the sign bit) and add it to the minuend (including the sign bit). A carry out of the sign bit position is discarded.
(±A) - ( + B) = (±A) + (- B )
(±A) - (- B) = (±A) + ( + B )

## Slide 70
Booth Multiplication (CO1)
1. Booth algorithm gives a procedure for multiplying binary integers in signed-2's complement representation.
2. It operates on the fact that strings of O's in the multiplier require no addition but just shifting, and a string of 1's in the multiplier from bit weight 2' to weight 2m can be treated as 2'+1 - 2m

## Slide 71
IEEE standard for Floating point numbers (CO1)
The IEEE Standard for Floating-Point Arithmetic (IEEE 754) is a technical standard for floating-point arithmetic established in 1985 by the Institute of Electrical and Electronics Engineers (IEEE). ... rounding rules: properties to be satisfied when rounding numbers during arithmetic and conversions.

## Slide 72
Daily Quiz
Show the step-by-step multiplication process using Booth algorithm when the following binary numbers are multiplied. Assume 5-bit registers that hold signed numbers. The multiplicand in both cases is +15.
a. ( + 15) x ( + 13)
b. ( + 15) X ( - 13)
2. Represent – (0.75) into IEEE 754 standard for single precision and double precision.

## Slide 73
Weekly Assignment
1. A sequential circuit has two D flip-flops A and B, two inputs x and y, and one output z. The flip-flop input equations and the circuit output are as follows:
DA= x'y + xA
DB = x ‘B + xA
z = B
a. Draw the logic diagram of the circuit.
b. Tabulate the state table.
2. Show the contents of registers E, A, Q, and SC (as in Table 10-2) during the process of multiplication of two binary numbers, 11111 multiplicand) and 10101 (multiplier). The signs are not included.
3. Show the contents of registers E, A, Q, and SC (as in Fig. 10-12) during the process of division of (a) 10100011 by 1011; (b) 00001111 by 0011 . (Use a dividend of eight bits.)

## Slide 74
Glossary
1. Single choice questions (Glossary)
(Transistor, Cache, D, 1)
a. 1 + x = --------.
b. ---------- type of materials used in second generation.
c. Hexa decimal of 13 is ----------.
d. ---------------- memory is placed in between main memory and CPU.
2. (Bus, Secondary, Invertor, Universal gate)
Magnetic is -------------- type memory.
The communication line between the CPU, memory and other devices is called -------------.
NAND and NOR are called -----------.
A NOT gate is also known as -------------.

## Slide 75
Glossary
(word size,1, Instruction Set, Accumulator)
-------------- is a general purpose processing register.
The length of a register is called _______.
The number of sign bits in a 32-bit IEEE format __________.
CPU has built-in ability to execute a particular set of machine instructions, called as __________.
4.

## Slide 76
YouTube/other Video Links
https://www.youtube.com/watch?v=yKPD_UkbgXo
https://www.youtube.com/watch?v=CDO28Esqmcg
https://www.youtube.com/watch?v=SZu2pchW54Q
https://www.youtube.com/watch?v=L9X7XXfHYdU&list=PLxCzCOWd7aiHMonh3G6QNKq53C6oNXGrX
Faculty Video Links, YouTube & NPTEL Video Links and Online Courses Details

## Slide 77
1. The ______ format is usually used to store data. a) BCD b) Decimal c) Hexadecimal d) Octal
2. The 8-bit encoding format used to store data in a computer is _____ a) ASCII b) EBCDIC c) ANCI d) USCII
3. Which memory device is generally made of semiconductors? a) RAM b) Hard-disk c) Floppy disk d) Cd disk
4. The small extremely fast, RAM’s are called as _______ a) Cache b) Heaps c) Accumulators d) Stacks
5. The I/O interface required to connect the I/O device to the bus consists of ______ a) Address decoder and registers
b) Control circuits c) Address decoder, registers and Control circuits d) Only Control circuits
Multiple Choice Questions

## Slide 78
http://www.aktuonline.com/papers/mca-1-sem-computer-organization-and-architecture-rca-104-2018-19.html
http://www.aktuonline.com/papers/mca-1-sem-computer-organization-and-architecture-rca-104-2017-18.html
http://www.aktuonline.com/papers/mca-1-sem-computer-organization-and-architecture-rca-104-2016-17.html
Old Question Papers

## Slide 79
Expected Questions for University Exam
Q-1. Perform the arithmetic operation (+42) + (-77) using 2,s complement representation for negative numbers.
Q-2. Define (r-1)’s complement with example.
Q-3. Represent decimal numbers from 0 to 9 in Excess-127 binary code.
Q-4. Determine by means of a truth table the validity of DeMorgan’s theorem for three variables: (A+B+C)’ =A’.B’. C’
Q-5.Simplify the following Boolean functions using three variable maps.
F(x,y,z) =∑(0,1,5,7)
F(x,y,z)= ∑(0,2,3,4,6)
Q-6. Explain all logic gates with symbol, algebraic expression and truth table.

## Slide 80
Summary
As the technology of ICs has improved, the number of gates that can be put in a single chip has increased considerably.
Very large scale integration (VLSI) devices contain thousands of gates within a single package. Examples are large memory arrays and complex microcomputer chips.
Various types of registers are available commercially, the simplest register is one that consists only of flip flop, with no external gates.
A flip-flop is a binary cell capable of storing one bit of information.
The algebraic operation symbol of the AND function is the same as the multiplication symbol of ordinary arithmetic.
OR operation is like arithmetic addition, but the output must be 0 or 1.
A buffer does not produce any particular logic function. This circuit is merely used for power amplification.

## Slide 81
References
1. Logic and Digital Design, Morris mano and Kimicharels 4th Edition, Prentice Hall.
2.Computer System Architecture, M.Mano(PHI)
3.Computer Organization, Vravice, Zaky&Hamacher (TMH Publication)
4. Structured Computer Organization, Tannenbaum(PHI)
5. Computer Organization, Stallings(PHI)
6. Computer Organization, John P.Hayes (McGraw Hill)
Thank You